## Slide 1
Innovation is in our lifeblood

## Slide 2: Endtest Analysis and Reccomendations
By Austin Ibele

## Slide 3: Agenda
Methods
Limitations
Process flow
Overview of Recommendations
Detailed Recommendations

## Slide 4: Methods
1st: General interviews
2nd: Review of all test documentation (Chiller, Controller, Endtest, etc)
3rd /4th : Asking specific questions/Observation/Understanding tests
3rd /4th : Root Cause Analysis of Quality Complaints
Conclusion: Lets save time and make it more difficult to make mistakes

## Slide 5: Limitations
Scarce process performance data makes root cause analysis and optimization difficult
Large reduction in Endtest difficult since products must be tested as system
We will always have manual steps that are prone to error

## Slide 6: Types of Quality Problems
Chart: Problems
| 1. Quartal | 2. Quartal | 3. Quartal | 4. Quartal
Verkauf | 8.2 | 3.2 | 1.4 | 1.2
Coming soon…
Notes: Need to finish doing this..

## Slide 7: Endtest Process Flow
Chuck from Chuck Department
Controller from Cont. Department
Chiller from Chiller Department
Heating/Cooling
Curves & Temperature
Uniformity
Noise Testing
Steps
Fi
Final Planarity testing at Chuck Department
Temp Display/PT100 Calibration
Packing
Shipping

## Slide 8: Overview of Reccomendations
Documentation
  Collect Data
  Document Processes
  Verify Packing-lists and enter into SAGE
  Tablet for mobile data-entry
Optimization
  End duplicate temperature display calibration
  Electric screwdriver
  New temperature uniformity protocol to reduce human error
  Modify steps protocol
Automation
  “Doc Generator V2”/XLS data validation
  Automate temperature uniformity and heating/cooling curves
  Label printer
  Automate temperature display calibration
  Programmatically find steps abnormalities
Process Change
  New controllers for Chuck department and more intensive testing
  Final visual check/signoff
  Separate person for packing/shipping/system inspection

## Slide 9: Documentation-Related Suggestions

## Slide 10: Collect Data
What:
  Collect process performance data
How:
  Document all defects discovered in Endtest as well as corrections
  Save all test data, including data that does not meet product specifications
  Create form for written data-collection
  Create database/spreadsheet to store it
Why:
  Aid Root Cause Analysis
  Aid process optimization
  Assess process changes
How Much/Other:
  0 EUR capital investment
  Can implement immediately
  Minimal time to implement, minimal increase in Endtest work

## Slide 11: Document Process
What:
  Create documentation describing Endtest
How:
  Record process steps
  Create procedures documents
  May learn/assist with tests to help with documenting steps
Why:
  So other workers can perform Endtest duties
  Aid others in understanding/analyzing process
How Much/Other:
  0 EUR capital investment
  Moderate time investment
  Finish by end of May, 2019

## Slide 12: Verify Packing-lists and enter into SAGE
What:
  Verify Accuracy of Packing-Lists
  Attach Packing-Lists to systems in SAGE
How:
  Have „systems experts“ (z.b. Matthias) check accuracy of existing packing-lists
  Have someone add each packing-list to corresponding system in SAGE
Why:
  Many complaints about missing/wrong parts
  Root cause is often incorrect or incomplete packing-lists
How Much/Other:
  0 EUR capital investment
  Moderate time investment
  Unknown time to complete?

## Slide 13: Tablet for mobile data-entry
What:
  Use tablet/hand-held computer to enter all data for Endtest documents
How:
  Create data-collection forms with data-validation
  Enter test results/other information into tablet
  Likely windows tablet for use with server (Need to research..)
Why:
  Written results sometimes out of spec
  Difficult to read
  Errors when performing „mental math“
  Doesn‘t look as good
How Much/Other:
  200-300 EUR capital investment/tablet
  Moderate time investment
  Possible to finish by end May, 2019
Notes: https://www.amazon.com/Windows-Fusion5-Ultra-Design-Tablet/dp/B00YCX7SGU/ref=sr_1_3?keywords=windows+10+tablet&qid=1552466918&s=electronics&sr=1-3

## Slide 14: Optimization-Related Suggestions

## Slide 15: End duplicate temperature display calibration
What:
  Stop performing display calibration protocol twice
How:
  Make controller/chiller department keep performing calibration and verify in-spec
  Have Endtest stop performing this test
Why:
  This test is performed twice for no good reason (once in chiller/controller
  department, again in Endtest)
  If controller/chiller department measures out-of-spec, they leave it out-of-spec
  for Endtest to fix
How Much/Other:
  0 EUR capital investment
  Can implement immediately
  Will require more time for Chiller/Controller department
  Will save a greater amount oftime in Endtest

## Slide 16: Electric Screwdriver
What:
  Electric screwdriver to save time
How:
  Equip departments with electric screwdrivers
  Many models exist, suitable for small electronics to large machines
Why:
  Dissamebly/assembly often required to fix/trouble-shoot in Endtest
  Almost all departments spend a significant time using screwdrivers
How Much/Other:
  30-100 EUR capital investment/screwdriver
  Can implement immediately
  Minimal time to implement

## Slide 17: New temperature uniformity protocol to reduce human error
What:
  Reduce hand-written errors on documents
How:
  Increase size of spaces for writing
  New/modified document
Why:
  Handwriting sometimes difficult to read
  Out-of-spec numbers not noticed
How Much/Other:
  0 EUR capital investment
  A few hours time investment
  Can implement < 4 weeks

## Slide 18: Modify Steps Protocol
What:
  Save time OR
  Increase sensitivity of test
How:
  Reanalyze all recent steps
  Begin saving data on failed steps for analysis
  Document when steps fail
  Maybe change step intervals/duration to save time/increase accuracy
Why:
  Steps are arbitarily defined
  Not data-based, so possible room for improvement
How Much/Other:
  0 EUR capital investment
  Need to wait for sufficient data to implement
  Implementation in > 3 months?

## Slide 19: Automation-Related Suggestions

## Slide 20: ”Doc Generator V2”/XLS data validation
What:
  Further improve accuracy/time savings of „Endtest Document Generator“ tool
How:
  Merge many PDFs into a single document for eaiser printing
  Create macros in „Seriennummern“ spreadsheet to prevent entry of wrong information
  Pipe data from Auftragsliste to Seriennummern XLS
Why:
  Opening and printing all different documents still time consuming
  Errors in Doc Generator output result from Seriennummern XLS input errors
  Easy to accidently make input error into Seriennummern XLS
How Much/Other:
  0 EUR capital investment
  Moderate time to implement
  Can implement in < 4 weeks

## Slide 21: Automate temperature uniformity and heating/cooling curves
What:
  Automate determination of heating/cooling time and uniformity profile
How:
  Paddy will create new option in software to run heating/cooling and
  steps together
  Sensarray Wafer will collect data overnight while running tests
  New computer program will analyze Sensarray data and determine
  heating/cooling time and temperature uniformity
Why:
  Temperature uniformity performed during heating/cooling curves
  Time consuming process
How Much/Other:
  0 EUR capital investment
  Can implement immediately
  Minimal time to implement, minimal increase in Endtest work

## Slide 22: Label Printer
What:
  Accurately make labels with a label printer
How:
  Print serial number labels from serial number in seriennummern spreadsheet OR
  Require double entry of serial number
  Print on high temperature labels with programmable thermal transfer printer
Why:
  Incorrect serial number on label is a common quality problem
  Save time by eliminating the tedious task of manually making labels
How Much/Other:
  ~500 EUR capital investment/printer
  ? EUR for new custom labels
  Moderate-Large time investment
  Finish by end May 2019

## Slide 23: Automate Temperature Display Calibration
What:
  Create new test program to guide/perform PT100 calibration protocol
How:
  Program records display values
  Adjusts calibration curve by comparing to simulation data
  Test data goes into document (no more handwriting)
  Must be done by Paddy
Why:
  Time consuming (10 – 30 minutes depending on results)
  Some quality complaints on out-of-spec results written
How Much/Other:
  0 EUR capital investment
  High time investment/High Reward
  Defer to Paddy, who is the expert

## Slide 24: Programmatically find steps abnormalities
What:
  Identify system controlling problems (from steps data) automatically
How:
  Write program to analyze steps data and look for evidence of controlling problem
  Can be a separate program ran after the AC3 test program OR
  Integrated into AC3 test program by Paddy
Why:
  Possibly more accurate than humans (humans are great at pattern recognition
  , but can be distracted)
  Save time since graph no longer needs to be looked at closely
  Assess process changes
How Much/Other:
  0 EUR capital investment
  Unsure how accurate it would be, but confident and think it could be worth trying
  Best if integrated into AC3 test program

## Slide 25: Process Change-Related Suggestions

## Slide 26: New controllers for Chuck department and more intensive testing
What:
  Find controlling problems earlier with new controllers and different tests in Chuck Department
How:
  New controllers (z.b. SP110) for chuck department
  Computer for chuck department to run AC3 test software
  Replace uberschwing test with heating to 50C, 80C and
  controlling (reccomended by Paddy)
  *MAYBE CAN ALSO write program to find controlling errors and use with current SP72
Why:
  Endtest catches PT100 placement/controlling problems that Uberschwing test misses
  These problems often not noticed until steps test, which is performed almost last
  Currently using SP72 controller with only a LED readout of temperature
How Much/Other:
  Unknown (?) capital investment
  No/minimal increase in work for Chuck Department
  Chuck Department unhappy with current controllers and wants new ones
  Extremely easy to implement once you have new controllers/computers
SP110 Controller

## Slide 27: Final Visual Check/Sign-off
What:
  Have another employee visually inspect/sign-off on system
How:
  Add to duties of upstairs/Lager worker (better if they are disconnected from production process)
  Perform after testing and prior to packaging
Why:
  Loose screws, cosmetic problems, incorrect serial numbers are common problems
How Much/Other:
  0 EUR capital investment
  Can implement immediately
  No change to work of Endtest worker
  ~2-3 hours per week duty for upstairs worker

## Slide 28: Separate person for preparation/packing/shipping
What:
  Similar to previous reccomendation but with additional duties
How:
  Another employee focuses on preparation of materials, visual inspection, packing, shipping
  Separate from test duties of Nuhan
Why:
  Nuhan is the expert in test, so he should test
  Nuhan over-worked on shipping days
  Distracted from testing by additional duties
How Much/Other:
  Large investment if new hire
  Possibly combine this position with Pierre‘s old position?

## Slide 29
Interested in learning more? Contact us:
  E-Mail: info@ers-gmbh.de
  Web site: www.ers-gmbh.com
  Telephone: +49 8989 4132-0
Follow us on social media:
  Twitter: @ers_gmbh
  LinkedIn: https://de.linkedin.com/company/ers-electronic-gmbh
Press contact: Miguel Resendiz
  E-Mail: m.resendiz@ers-gmbh.de
  Telephone/Mobile: +49 8989 4132-143
Contact us

## Slide 30
Thank You